TBT Quickstart Guide

When you first power up the TBT (Text Based Terminal) unit a Quick Setup menu will appear.

Defining Network Settings

On the Quick Setup enter the method for assigning the unit an IP address, either DHCP for an automatic assignment, or Select No to enter a Static IP address provided by your Network Administrator.

Defining 5250 sessions and the iSeries/AS400

Under the heading I-SERIES/AS400 is where the 5250 Displays will be defined.  By default 2 sessions are selected, the unit can support up to 4 sessions in TBT mode.  A naming convention for the 5250 sessions is also available here if a specific name is needed for devices created on the host. The Hostname/IP of the iSeries/AS400 will also be defined in Host Name/IP field.

If a printer needs to be attached to the TBT, a 5250 printer emulation session can be defined with a specific device name and an appropriate driver selected for the printer.